## Slide 1: COMPUTER SECURITY AND NETWORKING

## Slide 2
IP ADDRESSING

## Slide 3: NUMBER SYSTEMS
Before we continue discussing the TCP/IP protocol stack and IP addressing, it’s really important for you to truly understand the differences between binary, decimal, and hexadecimal numbers, and how to convert one format into the other

## Slide 4: BINARY NUMBERS
So we’ll start with binary numbering. It’s pretty simple. The digits used are limited to either a 1 (one) or a 0 (zero), with each digit being called one bit (short for binary digit).
Typically, you count either 4 or 8 bits together, with these being referred to as a nibble or a byte, respectively.

## Slide 5: CONT…
The binary numbers are placed in a value spot: starting at the right and moving left, with each spot having double the value of the previous spot.

## Slide 6: CONT…
NIBBLE VALUES | BYTE VALUES
8 4 2 1 | 128 64 32 16 8 4 2 1
Table 1 shows the decimal values of each bit location in a nibble and a byte. Remember, a nibble is 4 bits and a byte is 8 bits.

## Slide 7: CONT…
This means that if a one digit (1) is placed in a value spot, then the nibble or byte takes on that decimal value, and adds it to any other value spots that have a one.
If a zero (0) is placed in a bit spot, then you don’t count that value.

## Slide 8: CONT…
Examples:
11111111 255
10010110 150
01101100 108

## Slide 9: IP ADDRESSING
One of the most important topics in any discussion of TCP/IP is IP addressing.
An IP address is a numeric identifier assigned to each machine on an IP network. It designates the specific location of a device on the network.

## Slide 10: CONT…
An IP address is a software address, not a hardware address—the latter is hard-coded on a Network Interface Card (NIC) and used for finding hosts on a local network.
IP addressing was designed to allow a host on one network to communicate with a host on a different network, regardless of the type of LANs the hosts are participating in.

## Slide 11: IP TERMINOLOGY
Bit: A bit is one digit, either a 1 or a 0.
Byte: A byte is 7 or 8 bits, depending on whether parity is used. For the rest of this lecture, always assume a byte is 8 bits.
Octet: An octet, made up of 8 bits, is just an ordinary 8-bit binary number. In this lecture, the terms byte and octet are completely interchangeable.

## Slide 12: CONT…
Network address: This is the designation used in routing to send packets to a remote network—for example, 10.0.0.0, 172.16.0.0, and 192.168.10.0.
Broadcast address: The address used by applications and hosts to send information to all nodes on a network is called the broadcast address. Examples include 255.255.255.255.

## Slide 13: Hierarchical IP Addressing Scheme
An IP address consists of 32 bits of information.
These bits are divided into four sections, referred to as octets or bytes, each containing 1 byte (8 bits).
You can depict an IP address using one of three methods:
                Dotted-decimal, as in 172.16.30.56
                Binary, as in 10101100.00010000.00011110.00111000
                Hexadecimal, as in AC.10.1E.38

## Slide 14: CONT…
The 32-bit IP address is a structured or hierarchical address, as opposed to a flat or nonhierarchical address.
hierarchical addressing was chosen for a good reason.
The advantage of this scheme is that it can handle a large number of addresses, namely 4.3 billion.

## Slide 15: CONT…
The reason to why flat addressing scheme it’s not used for IP addressing, relates to routing. If every address were unique, all routers on the Internet would need to store the address of each and every machine on the Internet.
This would make efficient routing impossible, even if only a fraction of the possible addresses were used.

## Slide 16: CONT…
The solution to this problem is to use a two- or three-level, hierarchical addressing scheme that is structured by network and host, or network, subnet, and host.
Rather than all 32 bits being treated as a unique identifier, as in flat addressing, a part of the address is designated as the network address, and the other part is designated as either the subnet and host or the node address.

## Slide 17: NETWORK ADDRESSING
The network address (which can also be called the network number) uniquely identifies each network
. Every machine on the same network shares that network address as part of its IP address. In the IP address 172.16.30.56, for example, 172.16 is the network address.
The node address is assigned to, and uniquely identifies, each machine on a network. This number can also be referred to as a host address. In the sample IP address 172.16.30.56, 30.56 is the node address.

## Slide 18: CONT…

## Slide 19: CONT…
CLASS A | Network | Host | Host | Host
CLASS B | Network | Network | Host | Host
CLASS C | Network | Network | Network | Host

## Slide 20: Network Address Range: Class A
The first bit of the first byte in a Class A network address must always be off, or 0. This means a Class A address must be between 0 and 127, inclusive.
A Class A network is defined in the first octet between 0 and 127, and it can’t be less or more.

## Slide 21: CONT…
Class A network addresses are one byte long, with the first bit of that byte reserved and the 7 remaining bits available for manipulation (addressing).
As a result, the maximum number of Class A networks that can be created is 128. Why? Because each of the 7-bit positions can be either a 0 or a 1, thus 128.

## Slide 22: CONT…
Each Class A address has three bytes (24-bit positions) for the node address of a machine.
This means there are 2^24—or 16,777,216—unique combinations and, therefore, precisely that many possible unique node addresses for each Class A network.

## Slide 23: CONT…
Because node addresses with the two patterns of all 0s and all 1s are reserved, the actual maximum usable number of nodes for a Class A network is 224 minus 2, which equals 16,777,214. Either way, that’s a huge amount of hosts on a network segment!

## Slide 24: Class A Valid Host IDs
All host bits off is the network address: 10.0.0.0.
All host bits on is the broadcast address: 10.255.255.255,The valid hosts are the numbers in between the network address and the broadcast address: 10.0.0.1 through 10.255.255.254.

## Slide 25: Network Address Range: Class B
In a Class B network, the first bit of the first byte must always be turned on, but the second bit must always be turned off.
If you turn the other 6 bits all off and then all on, you will find the range for a Class B network: 10000000 = 128 - 10111111 = 191.
A Class B network is defined when the first byte is configured from 128 to 191

## Slide 26: CONT…
With a network address being two bytes (8 bits each), there would be 2^16 unique combinations. However the Internet designers decided that all Class B network addresses should start with the binary digit 1, then 0.
This leaves 14-bit positions to manipulate, therefore 16,384 (that is, 2^14) unique Class B network addresses.

## Slide 27: Class B Valid Host IDs
All host bits turned off is the network address: 172.16.0.0.
All host bits are turned on is the broadcast address: 172.16.255.255.
The valid hosts would be the numbers in between the network address and the broadcast address: 172.16.0.1 through 172.16.255.254.

## Slide 28: Network Address Range: Class C
Class C networks, the first 2 bits of the first octet as always turned on, but the third bit can never be on.
Following the same process as the previous classes, convert from binary to decimal to find the range. Here’s the range for a Class C network: 11000000 = 192 - 11011111 = 223

## Slide 29: CONT…
In a Class C network address, the first three-bit positions are always the binary 110. The calculation is: 3 bytes, or 24 bits, minus 3 reserved positions, which leaves 21 positions.
Hence, there are 2^21, or 2,097,152, possible Class C networks.

## Slide 30: CONT…
Each unique Class C network has one byte to use for node addresses. This leads to 2^8 or 256, minus the two reserved patterns of all 0s and all 1s, for a total of 254 node addresses for each Class C network.

## Slide 31: Class C Valid Host IDs
All host bits turned off is the network ID: 192.168.100.0.
All host bits turned on is the broadcast address: 192.168.100.255.
The valid hosts would be the numbers in between the network address and the broadcast address: 192.168.100.1 through 192.168.100.254.

## Slide 32: CONT…
NOTE:
Notice that 0s and 255s can be valid host IDs. All you need to remember when trying to find valid host addresses is that the host bits can’t all be turned off or all be on at the same time.

## Slide 33: Network Address Ranges: Classes D and E
The addresses between 224 and 255 are reserved for Class D and E networks. Class D (224–239) is used for multicast addresses and Class E (240–255) for scientific purposes, but I’m not going into these types of addresses.